## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Control Flow and Pipelined MIPS
Instructor: Siddharth Garg

## Slide 2: CPU Performance Metrics
Instructions Per Cycle (IPC)
  IPC of the single-cycle MIPS: 1
  Can IPC be greater than 1? Yes: super-scalar processors
Let’s say CPU1 and CPU2 have the same IPC, but CPU1 runs at a faster clock frequency (small clock period). Which is better?
Instructions Per Second (IPS)
  (Instructions/Cycles x Cycles/Second) = (Instructions/Cycles x Clock Frequency)
  Single-Cycle MIPS IPS = 1 Inst/Cycle x (1 / 3 ns) = 0.33 Giga Instructions/second

## Slide 3: Improving Throughput: Pipelining
Module 1
Module 2
Module 3
Module 4
Flip-Flop
Flip-Flop
CLK
CLK
t1
t2
t3
t4
Throughput = 1/(t1+t2+t3+t4)
Module 1
Module 2
Module 3
Module 4
Flip-Flop
Flip-Flop
CLK
CLK
t1
t2
t3
t4
Throughput = ?
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK

## Slide 4: Pipeline Operation
Module 1
Module 2
Module 3
Module 4
Flip-Flop
Flip-Flop
CLK
CLK
t1
t2
t3
t4
Clock Period = max(t1,t2,t3,t4)
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
In steady state, each module processes data in parallel -> Throughput = 1 / max(t1,t2,t3,t4)

## Slide 5: Pipelining the Single-Cycle R-Type MIPS
Basic steps in executing an R-type instruction
  Instruction fetch (IF)
  Instruction Decode/Register File Read (ID/RF)
  Execute in ALU (EX)
  Write-back Result to RF (WB)
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
WB
(RF)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
For now we will ignore ld/st instructions!

## Slide 6
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
IF
ID/RF
EX
WB
Wrt Enable
Wrt Enable
15:11

## Slide 7
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
IF
ID/RF
EX
WB
Wrt Enable
Wrt Enable
15:11
0 ns
0 ns
0 ns
0 ns
1 ns
1 ns
1 ns
1 ns
1 ns
0 ns
0 ns
1 ns
Clock Period: 1 ns

## Slide 8
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
IF
ID/RF
EX
WB
Wrt Enable
Wrt Enable
15:11
Pipelined Control Signals

## Slide 9
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
IF
ID/RF
EX
WB
Wrt Enable
Wrt Enable
add $1, $2, $3
0
4
sub $4, $5, $6
$1
$2
1
add $1, $2, $3
8
and $7, $8, $9
sub $4, $5, $6
$5
$4
R[$1]
R[$2]
1
ADD
ADD
SUB
$3
$6
$3
12
add $10, $11, $12
and $7, $8, $9
$7
$8
$9
AND
SUB
R[$4]
R[$5]
$6
$3
R[$1]+R[$2]
1
0: add $1, $2, $3
4: sub $4, $5, $6
8: and $7, $8, $9
12: add $10, $11, $12

## Slide 10
IF
ID/RF
EX
WB
IF
ID/RF
EX
WB
IF
ID/RF
EX
WB
IF
ID/RF
EX
Time
Instructions
t0
t1
t2
t3
Inst0
Inst1
Inst2
Inst3

## Slide 11
IF
ID/RF
EX
WB
IF
ID/RF
EX
WB
IF
ID/RF
EX
WB
IF
ID/RF
EX
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
add $4 ,$5 ,$6
Read $1, $2
R[$1] + R[$2]
Write $3
Read $4, $5
R[$4] + R[$5]
Write $6
add $7, $8 ,$9
Read $7, $8
R[$7] + R[$8]
Write $9
Both access RF
add $6, $7 ,$9
Read $6, $7
Both access RF
(write happens before read)
Structural Hazard: two (or more) instructions accessing the same hardware module

## Slide 12
IF
ID/RF
EX
WB
IF
ID/RF
EX
WB
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
add $3 ,$5 ,$6
Read $1, $2
R[$1] + R[$2]
Write $3
Read $3, $5
R[$3] + R[$5]
Write $6
But $3 has not been written back to the register file yet!
Read-after-write (RAW) Hazard
(RAW Hazard is an example of a Data Hazard)

## Slide 13: Handling RAW Hazards
Solution 1
  Detect and avoid in software: compiler inserts nops (example: sll $0, $0, 0)
  Pros? Cons?
IF
ID/RF
EX
WB
IF
ID/RF
EX
WB
Time
add $1, $2, $3
nop
Read $1, $2
R[$1] + R[$2]
Write $3
IF
ID/RF
EX
WB
add $3 ,$5 ,$6
Read $3, $5
R[$3] + R[$5]
Write $6
nop
nop
nop

## Slide 14: Handling RAW Hazards
Solution 2
  Detect and avoid in hardware: stall the pipeline
  Pros? Cons?
IF
ID/RF
EX
WB
Time
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
Write $3
IF
ID/RF
EX
WB
add $3 ,$5 ,$6
Read $3, $5
R[$3] + R[$5]
Write $6
ID/RF
IF
and $7, $8, $9
IF
Read $3, $5
and $7, $8, $9

## Slide 15: Implementing Stalls
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
Read Address
Instruction
Instruction Memory
Adder
+4
ALU op
3
Wrt Enable
FLIP-FLOP
(PC)
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
IF
ID/RF
EX
WB
Wrt Enable
Wrt Enable
add $1, $2, $3
0
4
add $3, $5, $6
$1
$2
1
add $1, $2, $3
8
and $7, $8, $9
add $3, $5, $6
$5
$3
R[$1]
R[$2]
1
ADD
ADD
$3
$6
$3
$3
$3
R[$1]+R[$2]
0: add $1, $2, $3
4: add $3, $5, $6
8: and $7, $8, $9
12: add $10, $11, $12
STALL
STALL
1
nop
nop
nop
nop
nop
12
add $10, $11, $12
and $7, $8, $9
$8
$7
AND
R[$3]
R[$5]
$6
ADD
1
nop
nop
nop
$9

## Slide 16: Implementing Stalls: Details
Detect Stall in IF/ID stage by checking
  Destination register of previous inst. == source register of current inst
When Stall is detected
  PC flip-flop is “stalled” -> outputs the same value as in previous clock cycle
  ID/RF flip-flop is stalled
  Nop inserted in EX flip-flop
Stall clears in next clock cycle
Impact on IPC?
  10% of instructions have RAW dependencies
  Worst case?

## Slide 17: Handling RAW Hazards
Solution 3
  Forward data from the EX stage
  Pros? Cons?
IF
ID/RF
EX
WB
Time
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
Write $3
IF
ID/RF
EX
WB
add $3 ,$5 ,$6
Read $3, $5
R[$3] + R[$5]
Write $6

## Slide 18: Implementing Forwarding
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
ALU op
3
Wrt Enable
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
ID/RF
EX
WB
Wrt Enable
Wrt Enable
STALL
FwdRs?
IF STAGE NOT SHOWN
add $3, $5, $6
add $1, $2, $3
$3
$6
R[$1]
R[$2]
sum=R[$1]+R[$2]
0
0
add $3, $5, $6
1
0
$6
$3
and $7, $8, $9
sum
R[$5]
FwdRt?
R[$5]
R[$3]

## Slide 19: Forwarding Control
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
ALU op
3
Wrt Enable
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
ID/RF
EX
WB
Wrt Enable
Wrt Enable
STALL
FwdRs?
IF STAGE NOT SHOWN
FwdRt?
FwdRs? = 1 if destination register (rd) for inst in WB stage is same as source register (rs) for instruction in EX stage
FwdRt? = 1 if destination register (rd) for inst in WB stage is same as source register (rt) for instruction in EX stage
But we don’t know rs and rt in EX stage!

## Slide 20: Forwarding Control
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
ALU op
3
Wrt Enable
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
ID/RF
EX
WB
Wrt Enable
Wrt Enable
FwdRs?
IF STAGE NOT SHOWN
FwdRt?
rdID
rsID, rtID,
rdEX
rdWB
rsEX, rtEX,
If (rsEX==rdWB)
FwdRs?=1
Else
FwdRs?=0
If (rtEX==rdWB)
FwdRt?=1
Else
FwdRt?=0

## Slide 21: Handling RAW Hazards
Solution 3
  Forward data from the EX stage
  Impact on IPC (Instructions/cycle)?
  Impact on IPS (Instructions/second)?
IF
ID/RF
EX
WB
Time
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
Write $3
IF
ID/RF
EX
WB
add $3 ,$5 ,$6
Read $3, $5
R[$4] + R[$5]
Write $6

## Slide 22: Impact on Cycle Time
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
ALU op
3
Wrt Enable
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
ID/RF
EX
WB
Wrt Enable
Wrt Enable
FwdRs?
IF STAGE NOT SHOWN
FwdRt?
Muxes increase delay of EX stage

## Slide 23: 5 Stage Pipeline (with support for load/store)
Basic steps in executing an R-type instruction
  Instruction fetch (IF)
  Instruction Decode/Register File Read (ID/RF)
  Execute in ALU (EX)
  Load result from or store result to data memory (MEM)
  Write-back Result to RF (WB)
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK

## Slide 24
IF
ID/RF
EX
MEM
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
lw $4 ,$5, imm
Read $1, $2
R[$1] + R[$2]
nop
Read $4
Addr=R[$4] + SgnImm
Load from Addr
WB
Write $3
WB
Write $5
t5
IF
ID/RF
EX
MEM
sw $6 ,$7, imm
Read $6, $7
Addr=R[$6] + SgnImm
Store R[$7]
to Addr
WB
Nop

## Slide 25: RAW Hazards: Add-Add Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5
EX-EX Forwarding (same as 4-stage pipeline)

## Slide 26: RAW Hazards: Add-Add Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding
IF
ID/RF
EX
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5

## Slide 27: 5 Stage Pipeline (with support for load/store)
Two forwarding paths
  Same destination register in both forwarding paths? Pick data from EX-EX forwarding path
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Forwarding Control Logic
R[rd] from prior instruction
R[rd] from prior to prior instruction

## Slide 28: RAW Hazards: Add-Load Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
EX-EX Forwarding

## Slide 29: RAW Hazards: Add-Load Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4

## Slide 30: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
Will this work?
Solution: Stall the pipeline

## Slide 31: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
Solution: Stall the pipeline
EX
R[$4] + R[$5]

## Slide 32: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding