## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Pipelined MIPS
Instructor: Siddharth Garg

## Slide 2: Handling RAW Hazards in 4 stage Pipeline
Forwarding
IF
ID/RF
EX
WB
Time
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
Write $3
IF
ID/RF
EX
WB
add $3 ,$5 ,$6
Read $3, $5
R[$3] + R[$5]
Write $6

## Slide 3: Forwarding Control
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
ALU op
3
Wrt Enable
Decoder
FLIP-FLOP
FLIP-FLOP
FLIP-FLOP
ALU op
ID/RF
EX
WB
Wrt Enable
Wrt Enable
FwdRs?
IF STAGE NOT SHOWN
FwdRt?
rdID
rsID, rtID,
rdEX
rdWB
rsEX, rtEX,
If (rsEX==rdWB)
FwdRs?=1
Else
FwdRs?=0
If (rtEX==rdWB)
FwdRt?=1
Else
FwdRt?=0

## Slide 4: 5 Stage Pipeline (with support for load/store)
Basic steps in executing an R-type instruction
  Instruction fetch (IF)
  Instruction Decode/Register File Read (ID/RF)
  Execute in ALU (EX)
  Load result from or store result to data memory (MEM)
  Write-back Result to RF (WB)
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK

## Slide 5
IF
ID/RF
EX
MEM
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
lw $4 ,$5, imm
Read $1, $2
R[$1] + R[$2]
nop
Read $4
Addr=R[$4] + SgnImm
Load from Addr
WB
Write $3
WB
Write $5
t5
IF
ID/RF
EX
MEM
sw $6 ,$7, imm
Read $6, $7
Addr=R[$6] + SgnImm
Store R[$7]
to Addr
WB
Nop

## Slide 6: RAW Hazards: Add-Add Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5
EX-EX Forwarding (same as 4-stage pipeline)

## Slide 7: RAW Hazards: Add-Add Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding
IF
ID/RF
EX
MEM
add $3, $4, $5
Read $3, $4
R[$3] + R[$4]
nop
WB
Write $5

## Slide 8: 5 Stage Pipeline (with support for load/store)
Two forwarding paths
  Same destination register in both forwarding paths? Pick data from EX-EX forwarding path
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Forwarding Control Logic
R[rd] from prior instruction
R[rd] from prior to prior instruction

## Slide 9: 5 Stage Pipeline (with support for load/store)
Two forwarding paths
  Same destination register in both forwarding paths? Pick data from EX-EX forwarding path
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop
CLK
Forwarding Control Logic
R[rd] from prior instruction
R[rd] from prior to prior instruction

## Slide 10: RAW Hazards: Add-Load Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
EX-EX Forwarding

## Slide 11: RAW Hazards: Add-Load Dependency
IF
ID/RF
EX
MEM
Time
Instructions
t0
t1
t2
t3
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
t5
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4

## Slide 12: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
Will this work?
Solution: Stall the pipeline

## Slide 13: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
ID/RF
MEM
add $4, $5, $6
Read $4, $5
nop
WB
Write $6
Solution: Stall the pipeline
EX
R[$4] + R[$5]
IF
IF
ID/RF
EX
MEM
Read $4, $5

## Slide 14: RAW Hazards: Load-Add Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
Load from Addr
WB
Write $4
IF
ID/RF
EX
MEM
add $4, $5, $6
Read $4, $5
R[$4] + R[$5]
nop
WB
Write $6
IF
ID/RF
EX
MEM
add $7 $8, $9
Read $7, $8
R[$7] + R[$8]
nop
WB
Write $9
MEM-EX Forwarding

## Slide 15: RAW Hazards: Load-Store Dependency
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
R[$4] = Mem[Addr]
WB
Write $4
IF
ID/RF
EX
MEM
sw $5, $4, imm
Read $5
Mem[Addr] = R[$4]
WB
Write $9
MEM->MEM Forwarding
Addr = R[$5] + SgnImm

## Slide 16: Branch Instructions
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
IF
Assume that the branch condition is checked in ID/RF
Outcome of branch not known till cycle t2!

## Slide 17: Solution 1: Stall+Quash
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
Fetch from PC+4 by default
IF
ID/RF
EX
MEM
WB
PC+4
Taken
NOP
NOP
NOP
NOP
IF
ADDR

## Slide 18: What About RAW Dependencies?
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
nop
IF
ID/RF
EX
MEM
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
Result needed in ID/RF stage at the same time it is being computed

## Slide 19: What About RAW Dependencies?
Time
Instructions
t0
t1
t2
t3
t5
IF
ID/RF
EX
MEM
beq $3, $4, addr
Read $3, $4
R[$3]==R[$4]?
nop
WB
nop
nop
IF
ID/RF
EX
MEM
add $1, $2, $3
Read $1, $2
R[$1] + R[$2]
nop
WB
Write $3
New EX->ID/RF Forwarding Path
ID/RF
Read $3, $4
R[$3]==R[$4]?
FOR LAB1 YOU CAN ASSUME THAT THIS CASE NEVER ARISES! PROGRAMS WILL NOT HAVE BEQS WITH RAW DEPENDENCIES

## Slide 20: Lab 1 Discussion
In this Lab assignment, you will implement an cycle-accurate simulator for a 5-stage pipelined MIPS processor in C++. The simulator supports a subset of the MIPS instruction set and should model the execution of each instruction with cycle accuracy.
Instruction | Format | OpCode (hex) | Funct. (hex)
addu | R-Type (ALU) | 00 | 21
subu | R-Type (ALU) | 00 | 23
lw | I-Type (Memory) | 23 | -
sw | I-Type (Memory) | 2B | -
beq | I-Type (Control) | 04 | -
halt | Custom instruction | FF | 
You only need to support 6 instructions!

## Slide 21: Pipeline Structure
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Use RF class from Lab 0
Use Dmem class from Lab 0
Use Imem class from Lab 0
ALU class is overkill since we only need adds/subs

## Slide 22: Simulating a Pipeline
Module 1
Module 2
Module 3
Module 4
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
M3(r2) = r3
M2(r1) = r2
M4(r2) = r4
M5(r4) = r5
r1
for (clk=1; clk<MAX; clk++){
r1 = getnew();
r2 = M2(r1);
r3 = M3(r2);
r4 = M4(r3);
r5 = M5(r4);}
Does this work?
for (clk=1; clk<MAX; clk++){
r5 = M5(r4);
r4 = M4(r3);
r3 = M3(r2);
r2 = M2(r1);
r1 = getnew();}
Simulate in reverse order!

## Slide 23: Flip-flops: IF and ID/RF Stage
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop Name | Bit-width | Functionality
PC | 32 | Current value of PC
nop | 1 | If set, IF stage performs a nop
Flip-Flop Name | Bit-width | Functionality
Instr | 32 | 32-bit instruction read from IMEM
nop | 1 | If set, ID/RF stage performs a nop

## Slide 24: Digging Into the Skeleton Code
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
WB
(RF)
struct IFStruct {
bitset<32> PC;
bool nop;
};
struct stateStruct {
IFStruct IF;
IDStruct ID;
EXStruct EX;
MEMStruct MEM;
WBStruct WB;
};
Contains the state of ALL flip-flops
Contains the state of IF Flip-flops
main(){
stateStruct state, newState;
//Compute newState based on state
//newState.IF.pc = state.IF.pc+4;
state = newState;
}
State.WB
State.EX
State.MEM
State.IF
State.ID
newState.WB
newState.EX
newState.MEM
newState.IF
newState.ID

## Slide 25: Flip-flops: EX Stage
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop Name | Bit-width | Functionality
Read_data1, Read_data2 | 32 | 32-bit data values read from RF
Imm | 16 | 16-bit immediate for I-Type instructions. Don’t care for R-type instructions
Rs, Rt | 5 | Addresses of source registers rs, rt. Note that these are defined for both R-type and I-type instructions
Wrt_reg_addr | 5 | Address of the instruction’s destination register. Don’t care if the instruction does not update RF

## Slide 26: Flip-flops: EX Stage
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop Name | Bit-width | Functionality
alu_op | 1 | Set for addu, lw, sw; unset for subu
is_I_type | 1 | Set if the instruction is an i-type instruction
wrt_enable | 1 | Set if the instruction updates RF
rd_mem, wrt_mem | 1 | rd_mem is set for lw instruction and wrt_mem for sw instructions
nop | 1 | If set, EX stage performs a nop

## Slide 27: In Class Exercise
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop Name | Bit-width | Functionality
Wrt_reg_addr | 5 | Address of the instruction’s destination register. Don’t care if the instruction does not update RF
If (state.ID.Instr[31:26]==000000)
newState.EX.Wrt_reg_addr = state.ID.Instr[15:11]
Else
newState.EX.Wrt_reg_addr = state.ID.Instr[20:16]
Flip-Flop Name | Bit-width | Functionality
Instr | 32 | 32-bit instruction read from IMEM
nop | 1 | If set, ID/RF stage performs a nop
Compute
newState.EX.Write_reg_addr = f(state.ID.Instr)

## Slide 28: Flip-flops: MEM Stage
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop Name | Bit-width | Functionality
ALUresult | 32 | 32-bit ALU result. Don’t care for beq instructions
Store_data | 32 | 32-bit value to be stored in DMEM for sw instruction. Don’t care otherwise
Rs, Rt | 5 | Addresses of source registers rs, rt. Note that these are defined for both R-type and I-type instructions
Wrt_reg_addr | 5 | Address of the instruction’s destination register. Don’t care if the instruction does not update RF
wrt_enable | 1 | Set if the instruction updates RF
rd_mem, wrt_mem | 1 | rd_mem is set for lw instruction and wrt_mem for sw instructions
nop | 1 | If set, MEM stage performs a nop

## Slide 29: Flip-flops: WB Stage
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop Name | Bit-width | Functionality
Wrt_data | 32 | 32-bit data to be written back to RF. Don’t care for sw and beq instructions
Rs, Rt | 5 | Addresses of source registers rs, rt. Note that these are defined for both R-type and I-type instructions
Wrt_reg_addr | 5 | Address of the instruction’s destination register. Don’t care if the instruction does not update RF
wrt_enable | 1 | Set if the instruction updates RF
nop | 1 | If set, WB stage performs a nop

## Slide 30: nop bit function
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Flip-Flop Name | Bit-width | Functionality
nop | 1 | If set, MEM stage performs a nop
If (state.WB.nop)
break; //doNothing
Else
//Code for WB stage
If the nop bit is set for any stage, the stage does not update architectural state. Importantly:
  IF does not update PC
  MEM does not perform stores
  WB does not update RF

## Slide 31: nop bit propagation
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
if(state.ID.nop==1)
nextState.EX.nop=1;
else
//We might still want to set nextState.EX.nop to 1 in case the ID stage stalls
If the nop bit for a stage is set, the nop bit for the subsequent stage should be set in the next clock cycle.
Example: determine nextState.EX.nop as a function of state.ID.nop

## Slide 32: In Class Exercise: Implement Forwarding
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
Forwarding Control Logic
R[rd] from prior instruction
R[rd] from prior to prior instruction
Let the ALU operands be Op1 and Op2. Write code to determine Op1 in terms of the current state of flip-flop registers. Assume all nop bits are 1. You might need:
  state.EX.Rs, state.EX.Read_data1
  state.MEM.Write_reg_addr, state.MEM.Write_reg_enable
  state.MEM.ALUresult
  state.WB.Write_reg_addr, stateWB.Write_reg_enable
  State.WB.Wrt_data
Op1 = state.EX.Read_data1;
If (state.WB.Write_reg_enable)
if(state.WB.Write_reg_addr==state.EX.Rs)
Op1 = state.WB.Wrt_data;
If (state.MEM.Write_reg_enable)
if(state.MEM.Write_reg_addr==state.EX.Rs)
Op1 = state.MEM.ALUresult;

## Slide 33: RAW Hazards: Load-Store Dependency
IF
ID/RF
EX
MEM
lw $3, $4, imm
Read $3
Addr = R[$3] + SgnImm
R[$4] = Mem[Addr]
WB
Write $4
IF
ID/RF
EX
MEM
sw $5, $4, imm
Read $5
Mem[Addr] = R[$4]
WB
Write $9
Stall + MEM-EX Forwarding
Addr = R[$5] + SgnImm
ID/RF
Read $5
Step 1: Stall the IF and ID/RF Flip-flops
by making sure they don’t update their state
if(stall){
newState.IF = state.IF;
newState.ID = state.ID;
}
Step 2: Push a nop to the EX stage
if(stall){
newState.EX.nop = 1;
}

## Slide 34: Halt Instruction
Assume the halt instruction is fetched at PC = N. The halt instruction signals the end of your simulation, once it has made its way through the pipeline.
When an halt instruction is fetched in the IF stage, your code must:
  Set the nop bit of the IF stage to 1
  Must NOT update the PC
This means that the we will check for the opcode of the halt instruction in the IF stage, not in the ID/RF stage.
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
halt
nop=0
PC=N

## Slide 35: Halt Instruction
Assume the halt instruction is fetched at PC = N. The halt instruction signals the end of your simulation, once it has made its way through the pipeline.
When an halt instruction is fetched in the IF stage, your code must:
  Set the nop bit of the IF stage to 1
  Must NOT update the PC
This means that the we will check for the opcode of the halt instruction in the IF stage, not in the ID/RF stage.
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
halt
nop=1
PC=N
nop=1

## Slide 36: Halt Instruction
Assume the halt instruction is fetched at PC = N. The halt instruction signals the end of your simulation, once it has made its way through the pipeline.
When an halt instruction is fetched in the IF stage, your code must:
  Set the nop bit of the IF stage to 1
  Must NOT update the PC
This means that the we will check for the opcode of the halt instruction in the IF stage, not in the ID/RF stage.
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
halt
nop=1
PC=N
nop=1
nop=1

## Slide 37: Halt Instruction
Assume the halt instruction is fetched at PC = N. The halt instruction signals the end of your simulation, once it has made its way through the pipeline.
When an halt instruction is fetched in the IF stage, your code must:
  Set the nop bit of the IF stage to 1
  Must NOT update the PC
This means that the we will check for the opcode of the halt instruction in the IF stage, not in the ID/RF stage.
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
halt
nop=1
PC=N
nop=1
nop=1
nop=1

## Slide 38: Halt Instruction
Once all nop bits are 1, you can quit the simulation!
IF
(PC, Imem)
ID/RF
(Decoder, RF)
EX
(ALU)
MEM
(Dmem)
Flip-Flop
Flip-Flop
CLK
CLK
Flip-Flop
CLK
Flip-Flop
CLK
Flip-Flop
CLK
WB
(RF)
halt
nop=1
PC=N
nop=1
nop=1
nop=1
nop=1