## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Introduction and Instruction Set Architectures (ISA)
Instructor: Siddharth Garg

## Slide 2: ISAs are Abundant
x86
x86-64
IA64
x86
x86-64 (AMD64)
T32 (Thumb)
A32 (ARM)
A64 (ARM-64)
PowerPC
MIPS32
MIPS64
VAX
SPARC
CISC
ISAs
RISC ISAs
Alpha
IBM360
Laptop
Desktop
Laptop
Desktop
Servers
Servers
Mobile
Servers
Laptop
Desktop
Embedded

## Slide 3: ISA Design: Instruction Length
An instruction is a basic unit of an ISA
Fixed versus variable length instructions
  Fixed: Each instruction in the MIPS ISA is 32 bits (4 Bytes) long
  Variable: x86 instructions vary from 1 to 17 Bytes long
32 bits
8 bits
136 bits
Typical of RISC ISAs
Typical of CISC ISAs
Trade-offs?
Notes: Imagine a book written without spaces. Would it be useful if each word had the same length?

## Slide 4: ISA Design: Operand Addresses
ALU
(+, -, x)
Where do the operands come from?
Where is the result written?
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Instruction specifies 2 source and 1 destination register
“3-Address” ISA (E.g., MIPS ISA)
add rs, rt, rd
($rd ←$rs + $rt)
Value of register rt
Example:
add r1, r2, r3
Add content of registers r1 and r2 to register r3

## Slide 5: 1- and 2-Address ISAs
Write result back to a source register
“2-Address” ISA
(Have we seen an example today?)
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Special purpose “Accumulator” serves as an operand and as the destination
“1-Address” ISA
(Also called an “Accumulator Architecture”)
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator

## Slide 6: Add Routine for 2-Address ISA
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
add rs, rd
($rd ←$rd + $rs)
sub rs, rd
($rd ←$rd - $rs)
sub r3, r3 //$r3=0
Write code to add contents of registers r1 and r2 to register r3
add r1, r3 //$r3=r1
add r2, r3 //$r3=r1+r2

## Slide 7: Swap Routine for 1-Address ISA
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator
add rs
($acc ←$acc + $rs)
sub rs
($acc ←$acc - $rs)
mvto rs
($rs ←$acc )
mvfrm rs
($acc ←$rs)
mvfrm r1 //acc=$r1
add r2 //acc=$r1+$r2
mvto r3 //$r2=$r1+$r2
Write code to add contents of registers r1 and r2 to register r3

## Slide 8: So Which is “Better”?
add r1, r2, r3
Metrics?
  Code size (Bytes)
  Design complexity
Assume 5-bit opcode for all 3 ISAs
How many bits requires to address 32 registers?
Code size = Num Insts x Bits/Inst
  3-Address ISA
  2-Address ISA
  1-Address ISA
sub r3, r3 //$r3=0
add r1, r3 //$r3=r1
add r2, r3 //$r3=r1+r2
mvfrm r1 //acc=$r1
add r2 //acc=$r1+$r2
mvto r3 //$r2=$r1+$r2

## Slide 9: So Which is “Better”?
Metrics?
  Code size (Bytes)
  Design complexity
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
2 Read ports
1 Write port
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
Accumulator
1 Read port
1 Write port
1 R/W accum

## Slide 10: How is Memory Accessed
Can also be bit-addressable, 32-bit addressable, 64-bit addressable, etc.
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
byte 1
byte 2
byte N
Array of Bytes
Main Memory
Addr
Mem[Addr]
“Byte addressable”
How many bits should Addr have?
{Mem[Addr], Mem[Addr+1], Mem[Addr+2], Mem[Addr+3]}

## Slide 11: Load-Store ISA
Instructions like add, sub etc. operate only on registers (examples: MIPS, ARM, 3/2/1/0-Address ISAs we have seen so far)
  Separate Load/Store instructions to fetch data from memory into registers and to write data back from registers to memory
Reg. File
Reg. 0
Reg. 1
Reg. 31
ALU
(+, -, x)
byte 1
byte 2
byte N
Array of Bytes
Main Memory
add rs, rt, rd
($rd ←$rs + $rt)
load rt, M
($rt ←Mem[M])
store rt, M
( Mem[M] ←$rt )
Load data at memory location M
into register rt
Store data in register rt to memory location M

## Slide 12: Memory-Memory ISA
Allow instructions like add/sub to operate directly on data in memory (Examples include: x86, VAX etc.)
Most generally, each of the two operands and the result can be read-from/written-to either memory or register file
  Pros?
  Cons?
add Ms, Mt, Md
(Mem[Md] ←Mem[Ms] + Mem[Mt])
Memory address

## Slide 13: Addressing Modes
How to specify where to read from/write to
Orthogonal ISA: each op supports every addressing mode (ex: VAX)
load rt, M
($rt ←Mem[M])
Absolute
load rs, rt
($rt ←Mem[$rs])
Register Indirect
load rs, rt, offset
($rt ←Mem[offset+$rs])
Displaced/Based
Directly provide memory address
Memory address from register rs
Add an offset to address stored in register rs
load rs, rt, rd
($rd ←Mem[$rs + $rt])
Indexed
load rt, rs
($rt ←Mem[Mem[$rs]]
Memory Indirect
load rt, rs
($rt ←Mem[$rs]
$rs ←$rs + 1)
Auto-increment
Base memory address and offset from registers
Use value at Mem[$rs] as address
Same as Register indirect + value in rs is automatically incremented

## Slide 14: What Makes a Good ISA
Ease of hardware implementations
  Decoder for fixed vs. variable instruction lengths
  Simple vs. complex addressing modes
Ease of software implementation
  Can the programmer/compiler use the ISA easily?
  How many assembly instructions to represent a single line of code in a high-level language? “semantic gap”
Backwards compatibility
  ISA will have to be supported into the future; new instructions can be added but existing instructions cannot be removed

## Slide 15: CISC Vs. RISC
CISC: “Complex” Instruction Set Computer
RISC: “Reduced” Instruction Set Computer
  Each CISC instruction = multiple RISC instructions
CISC vs. RISC debate dominated the 80s/early 90s but is largely resolved now
  CISC ISAs like x86 are “broken down” internally into simpler RISC-like instructions (microcode)
  x86 is “externally CISC but internally RISC”
  Other popular ISAs like ARM and MIPS are RISC

## Slide 16: ISA Comparison
 | VAX | x86 | MIPS
ISA Type | CISC | CISC (but internally RISC) | RISC
Instruction Length | Variable | Variable | Fixed
Addressing Modes | 3-Address; memory-memory; orthogonal addressing modes | 2-Address; register-memory | 3-Address; load/store ISA

## Slide 17: MIPS ISA Overview
32-bit ISA (what does this mean?)
  Instruction length: 32 bits
  Data word length: 32 bits
32 general purpose registers ($0, $1, $2, … $31); 32-bits each
  Register $0 is hard-wired to 0 (constant)
  All other registers can be used as read/write
  But, certain registers dedicated for specific purposes by compiler
    Global pointer ($28), Stack pointer ($29), Frame pointer ($30), Return Address ($31)
    We wont worry about these conventions in this class!
Two dedicated 32-bit registers hi and lo for multiplication ops
Separate regs/unit for floating point ops (discussed later)

## Slide 18: MIPS Instructions: R-Type
add rs, rt, rd // R[rd] ← R[rs] + R[rt]; signed addition; trap on overflow
sub rs, rt, rd // R[rd] ← R[rs] - R[rt]; signed subtraction; trap on overflow
or rs, rt, rd // R[rd] ← R[rs] | R[rt]; bit-wise Boolean OR operation
sll rt, rd, shamt // R[rd] ← R[rt] << shamt; logical shift left
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
11
Rd
(5-bits)
10
Shamt
(5-bits)
6
5
funct
(6-bits)
0
000000 for all R-type instructions
Operand register identifiers
Result register identifier
Shift amount
Add: 100000 = 20hex
Sub: 100010 = 22hex
Or: 100101 = 25hex
Sll: 000000 = 00hex

## Slide 19: MIPS Instructions: R-Type
add rs, rt, rd // R[rd] ← R[rs] + R[rt]; signed addition; trap on overflow
Example assuming 4-bit datawords:
R[rs] = 0010 (2)
R[rt] = + 0111 (7)
= 1001 (-7)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
11
Rd
(5-bits)
10
Shamt
(5-bits)
6
5
funct
(6-bits)
0
000000 for all R-type instructions
Operand register identifiers
Result register identifier
Shift amount
Overflow occurs when the result of addition is not in the range [-8,7]
How to detect overflow?
If (MSB(R[Rs])== MSB(R[rt))
if (MSB(R[rd] != MSB(R[rt])
overflow!

## Slide 20: MIPS Instructions: I-Type
addi rs, rt, imm // R[rt] ← R[rs] + {SignExtend, imm}; MSB of imm is extended to 32 bits
beq rs, rt, imm // if{R[rs] == R[rt]} branch to PC + 4 + BranchAddress; (“PC relative”)
//BranchAddress = {signextendimm,imm[15:0],00}
ori rs, rt, imm // R[rt] ← R[rs] | {ZeroExtend,imm}; bit-wise Boolean OR operation
lw rs, rt, imm // R[rt] ← Mem[ {SignExtendimm} + R[rs] ] (“Displaced/based”)
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
Immediate
(16-bits)
0
Operand register
Immediate operand
addi: 8hex
beq: 4hex
ori: 25hex
lw: 23hex
Result register
(“PC relative”)

## Slide 21: MIPS Instructions: J-Type
j address // PC ← JumpAddress
jal address // R[31] ← PC+8; PC ← Jumpaddress;
//JumpAddress = { PC+4[31:28], address, 2’b0 }
// Also, R-type jump
jr rs // PC ← R[rs]
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
Immediate operand
j: 2hex
jal: 3hex

## Slide 22: Implementation of the MIPS ISA
Hardware building blocks
PC
Program Counter
A 32-bit “register”
(can store information)
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
Wrt Enable
Register File
32 32-bit registers
(2 Read ports, 1 Write Port)
5 bit address
5 bit address
5 bit address
32 bit data
32 bit data
32 bit data
Set to ‘1’ to enable write
result
ALU op
? bits
oprnd1
oprnd2
32 bits
32 bits
32 bits
Add: 20hex
Addu: 21hex
Sub: 23hex
Subu: 24hex
And: 25hex
Or: 24hx
Nor: 27hex
Arithmetic/Logic Unit (ALU)

## Slide 23: Implementation of the MIPS ISA
Hardware building blocks
Is this a von Neumann architecture?
Read Address
Instruction
Instruction Memory
(Read only)
32 bits
32 bits
Address
Write
Data
Read Data
Data Memory
Read Mem
Write Mem
32 bits
32 bits
32 bits
Set to ‘1’ to enable read; 0 otherwise
Set to ‘1’ to enable write; 0 otherwise
Data Memory
(Either read or write, but not both together)

## Slide 24
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
R-Type ALU Instructions

## Slide 25
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
I-Type ALU Instructions
20:16
Sign
Extend
15:0
32
Rs

## Slide 26
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
15:11
Adder
+4
ALU op
3
Wrt Enable
1
Combined R-Type and
I-Type ALU Instructions
20:16
Sign
Extend
15:0
MUX
a
b
control
a:b?control
I-Type?
I-Type?

## Slide 27
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ADD
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
Read Mem
Write Mem

## Slide 28
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ADD
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
IsLoad?
0

## Slide 29
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ADD
3
Wrt Enable
1
I-Type Store
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Did we miss something?
0

## Slide 30
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ADD
3
Wrt Enable
I-Type Store
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
!IsStore?