## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Single Cycle MIPS Implementation
Instructor: Siddharth Garg

## Slide 2: MIPS Instructions: R-Type
add rs, rt, rd // R[rd] ← R[rs] + R[rd]; signed addition; trap on overflow
sub rs, rt, rd // R[rd] ← R[rs] - R[rt]; signed subtraction; trap on overflow
or rs, rt, rd // R[rd] ← R[rs] | R[rt]; bit-wise Boolean OR operation
sll rt, rd, shamt // R[rd] ← R[rt] << shamt; logical shift left
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
11
Rd
(5-bits)
10
Shamt
(5-bits)
6
5
funct
(6-bits)
0
000000 for all R-type instructions
Operand register identifiers
Result register identifier
Shift amount
Add: 100000 = 20hex
Sub: 100010 = 22hex
Or: 100101 = 25hex
Sll: 000000 = 00hex

## Slide 3
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
R-Type ALU Instructions
“Datapath”

## Slide 4
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
Example: Instruction at PC=0
000000
00001
.
.
00000
00001
00010
00011
11111
A21F FFB3
0000 0000
BB33 CD53
1242 221E
0001 0001
RF Contents
00010
00011
00000
010100
00001
00010
00011
0
A21F FFB3
BB33 CD53
1
0
4
4
A21F FFB3 | BB33 CD53

## Slide 5: MIPS Instructions: I-Type
addi rs, rt, imm // R[rt] ← R[rs] + {SignExtend, imm}; MSB of imm is extended to 32 bits
beq rs, rt, imm // if{R[rs] == R[rt]} branch to PC + 4 + Target; (“PC relative”)
ori rs, rt, imm // R[rt] ← R[rs] | {ZeroExtend,imm}; bit-wise Boolean OR operation
lw rs, rt, imm // R[rt] ← Mem[ {SignExtendimm} + R[rs] ] (“Displaced/based”)
…..(many others)
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
Immediate
(16-bits)
0
Operand register
Immediate operand
addi: 8hex
beq: 4hex
ori: 25hex
lw: 23hex
Result register
(“PC relative”)

## Slide 6
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
20:16
15:11
Adder
+4
ALU op
3
Wrt Enable
1
I-Type ALU Instructions
20:16
Sign
Extend
15:0
32

## Slide 7
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
PC
Read Address
Instruction
Instruction Memory
25:21
15:11
Adder
+4
ALU op
3
Wrt Enable
1
Combined R-Type and
I-Type ALU Instructions
20:16
Sign
Extend
15:0
MUX
a
b
control
a if (control = 1)
b if (control = 0)
I-Type?
I-Type?

## Slide 8
ALU
result
ALU op
3
Combined R-Type and
I-Type ALU Instructions
What about ALUop?
Add: 20hex = 0010 0000
Addu: 21hex= 0010 0001
Sub: 22hex= 0010 0010
Subu: 23hex= 0010 0011
And: 24hex= 0010 0100
Or: 25hx= 0010 0101
Nor: 27hex= 0010 0111
Addi: 8hex= 1000
Addiu: 9hex = 1001
Andi: chex= 1100
Ori: dhex= 1101
Function Field
OpCode
http://www-inst.eecs.berkeley.edu/~cs61c/resources/MIPS_Green_Sheet.pdf
Last 3 bits of function field or Op Code uniquely identify the ALU functionality!

## Slide 9
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = ?
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
Read Mem
Write Mem

## Slide 10
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
1
I-Type Load
Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
IsLoad?
0

## Slide 11
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
1
I-Type Store Instructions
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
In-Class Problem 2:
Did we miss something?
0
sw rs, rt, imm //M[R[rs]+SignExtendimm] ← R[rt]

## Slide 12
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp = 001
3
Wrt Enable
!(IsStore?)
Final Data-Path
(Excluding Control Flow Instructions)
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?

## Slide 13: MIPS Instructions: J-Type
j address // PC ← {PC+4[31:28], address, 00}
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
Immediate operand
j: 2hex
jal: 3hex

## Slide 14: Control Flow
J-Type Control Flow
  4 MSB bits taken from the 4 MSBs of PC+4
  Next 26 bits taken from the “address” field
  Last 2 bits are set to zero? (why?)
31
26
Op-code
(6-bits)
25
address
(26-bits)
0
j address // PC ← {PC+4[31:28], address, 00}, opcode=2hex

## Slide 15
PC
Read Address
Instruction
Instruction Memory
Adder
+4
J-Type Control Instruction
RF Onwards Not Shown
Concat
31:28
PC+4
25:0
00
J-Type?
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
25:21
15:11
Wrt Enable
20:16
15:0
I-Type?
!(IsStore?)
What about WrtEnable?
0
!(J-Type?)

## Slide 16: Control Flow
I-Type Branch Instruction
  First 30 MSBs from sign extended immediate
  2 LSBs are always 0
beq rs, rt, imm // If (R[rs]==R[rt])
// PC ← PC + 4 + {SignExtendImm, 00},
// else
// PC ← PC + 4
// opcode=4hex
31
26
Op-code
(6-bits)
25
21
Rs
(5-bits)
20
16
Rt
(5-bits)
15
Immediate
(16-bits)
0

## Slide 17
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
25:21
15:11
Wrt Enable
20:16
Sign
Extend
15:0
I-Type?
I-Type?
PC
Read Address
Instruction
Instruction Memory
Adder
+4
Concat
31:28
PC+4
25:0
00
NextPC? = function(J-Type?, IsBranch?, IsEq?)
Adder
PC+4
=
IsEq?
{SignExtendImm[29:0],00}
29:0
!(IsBranch?)
3:1 MUX

## Slide 18
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Generating Control Signals
(Control Path)
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
ALUOp
IsLoad?
IsStore?
I-Type?
Wrt Enable

## Slide 19
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
ALUOp
IsLoad? = (Inst[31:26] == 100011)
IsStore? = (Inst[31:26] == 101011)
I-Type? = (Inst[31:26] != 00000) && (Inst[31:26] != 00010)
Wrt Enable

## Slide 20
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
If (Inst[31:26] == 100011) | (Inst[31:26] == 101011)
ALUop = 001
Else
ALUop = Inst[2:0]
ALUOp
Does this cover all cases?

## Slide 21
Control Path
Instruction Fetch Part Not Shown
If (Inst[31:26] == 100011) | (Inst[31:26] == 101011)
ALUop = 001
Else If (Inst[31:26]==000000)
ALUop = Inst[2:0]
Else
ALUop = Inst[28:26]
Final Correct Implementation of ALU OP

## Slide 22
Rd Reg. 1
Rd Reg. 2
Wrt Reg.
Wrt Data
Read
Data 1
Read
Data 2
ALU
result
25:21
15:11
ALUOp
3
Wrt Enable
Control Path
20:16
Sign
Extend
15:0
I-Type?
I-Type?
Address
Write
Data
Read Data
Instruction
Inst[31:0]
Instruction Fetch Part Not Shown
Data Memory
IsLoad?
Read Mem
Write Mem
isStore?
isLoad?
Decoder
If (IsStore? | IsBranch? | J-Type?)
WrtEnable = 0
Else
WrtEnable = 1
WrtEnable
J-Type? = (Inst[31:26]==000010)
IsBranch? = (Inst[31:26]==000100)

## Slide 23
If (IsBranch? && isEQ?)
NextPC? = 2
else if (J-Type?)
NextPC? = 1
else
NextPC? = 0
In-Class Problem 3:
Write pseudo-code for NextPC?

## Slide 24: Now Let’s Look at Lab 0
Class RF implements a register file
Registers contains a vector (array) of 32-bit values
class RF
{
public:
….
private:
vector<bitset<32>> Registers;
}

## Slide 25: What is a “bitset”?
C++ standard template library (STL) class
Click here and go through some details:
www.cplusplus.com/reference/bitset/bitset

## Slide 26: What is a “vector”?
C++ standard template library (STL) class

## Slide 27: Register File
Function RF() is called every time a new object of class RF is instantiated
  Sizes the RF to 32 regs, sets $r0 to 0
class RF
{
public:
….
RF(){
Registers.resize(32);
Registers[0] = bitset<32> (0);
}
}

## Slide 28: Register File
ReadWrite function allows data to be written to and from the RF
class RF
{
public:
….
void ReadWrite(bitset<5> RdReg1, bitset<5> RdReg2, bitset<5> WrtReg, bitset<32> WrtData, bitset<1> WrtEnable)
{
// implement the function by yourself
}
}

## Slide 29: Write Operation
ReadWrite function allows data to be written to and from the RF
class RF
{
public:
….
void ReadWrite(bitset<5> RdReg1, bitset<5> RdReg2, bitset<5> WrtReg, bitset<32> WrtData, bitset<1> WrtEnable)
{
// What gets updated?
}
}

## Slide 30: Read Operation
ReadWrite function allows data to be written to and from the RF
class RF
{
public:
bitset<32> ReadData1, ReadData2;
void ReadWrite(bitset<5> RdReg1, bitset<5> RdReg2, bitset<5> WrtReg, bitset<32> WrtData, bitset<1> WrtEnable)
{
// How is the data read from RF accessed
}
}

## Slide 31: Note about addu Operation
Simply performs the standard addition algorithm on 2 32-bit values
  And ignores any carry-out
You can implement it bit-by-bit
  Or by converting bitsets to unsigned long ints (32 bit unsigned numbers) and adding them
  Hint: see what the C++ standard says about unsigned int addition

## Slide 32: Note about subu Operation
Inverts every bit of the second operand, adds to the first operand, and adds +1
  And ignores any carry-out
You can implement it bit-by-bit
  Or by converting bitsets to unsigned long ints (32 bit unsigned numbers) and subtracting them
  Hint: see what the C++ standard says about unsigned int subtraction