## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Advanced Caches
Instructor: Siddharth Garg

## Slide 2: Practical LRU Implementation
LRU is hard to implement in hardware for N>2
  Keep track of all possible N! orderings of N ways
  A linked list in which the head points to MRU and tail points to LRU
  Example: N=4; 4 x 2 bits = 8 bits per cache set and extra logic to update list on every access
Alternative policies that are more hardware friendly
  NOT MRU: same as LRU for N=2, requires only log(N) bits, easy update
  Hierarchical: for N=4, divide ways into 2 groups of 2 ways

## Slide 3: Hierarchical LRU Implementation
Way 0
Way 1
Way 2
Way 3
Group 0
Group 1
A
B
C
D
MRU Grp
MRU Way (G1)
MRU Way
(G0)
Sequence | A | C | D | B | A | A | E
MRU Grp | 0 | 1 | 1 | 0 | 0 | 0 | 
MRU Way (G0) | 0 | 0 | 0 | 1 | 0 | 0 | 
MRU Way (G1) | - | 2 | 3 | 3 | 3 | 3 | 
Which block is evicted?

## Slide 4: Hierarchical LRU Implementation
Way 0
Way 1
Way 2
Way 3
Group 0
Group 1
A
B
C
D
MRU Grp
MRU Way (G1)
MRU Way
(G0)
Sequence | A | C | D | B | A | D | E
MRU Grp | 0 | 1 | 1 | 0 | 0 | 1 | 
MRU Way (G0) | 0 | 0 | 0 | 1 | 0 | 0 | 
MRU Way (G1) | - | 2 | 3 | 3 | 3 | 3 | 
Which block is evicted?
Not the true LRU block!

## Slide 5: Exploiting Spatial Locality
Recall that if the byte from address i is accessed, then byte from address i+1 is likely to be accessed
  Pull in multiple contiguous bytes of data in each access
  Use larger block size!
Example: 32KB direct mapped cache with 8 Byte (64 bit) blocks
  i.e., cache has 4096 Byte blocks
Block 0
Block 4095
Data Array
(8 bytes)
Block 1
Index
(12 bits)
Offset
(3 bits)
Selects a byte from the block
Selects a block
Tag Array
(17 bits)
Tag 0
Tag 4095
Tag
(17 bits)
Valid

## Slide 6: Cache Operation
Block 0
Block 1
Block 2
Block 4095
Data Array
(8 bytes)
Tag 0
Tag 1
Tag 2
Tag 4095
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Address (32 bits)
V 2
=
MISS
0
&
1
0
HIT
1
Output Data if HIT
Index
(12 bits)
Offset
(3 bits)
Tag
(17 bits)
8 Bytes
8:1 MUX
1 Bytes

## Slide 7: Impact of Block Size
Sequence of addresses: A, A+1, A+2, A+3 …
  4 consecutive misses for 1 byte block size
  1 miss and 3 hits for 4 byte block size
Small block sizes don’t exploit any spatial locality
What happens if the block size increases for the same cache size
  Fewer number of larger blocks
[Source: D Brooks CS146 Lecs]

## Slide 8: In Class Exercise 1
Determine the number of offset bits, index bits and tag bits for a 4-way, 8KB cache with 8 Byte blocks. Assume that the cache is Byte addressable with a 32 bit address.
  Offset: 3 bits (8 byte blocks that are byte addressable)
  Number of sets: 213 bytes / ( 4 ways x 8 bytes per way) = : 213 bytes / 25 bytes = 28 sets
  Index: 8 bits
  Tag: 32 – 8 – 3 = 21 bits

## Slide 9: Write Policies
What should we do on a cache store/write access
  Cannot perform tag look-up and data-array lookup in parallel (why?)
  First access tag array and if there is a write hit, write to the data array
  Increases the delay of a cache access (recall: period is determined by the worst-case)
What do on a write hit?
  When there is a tag match (i.e., block exists in cache)
What to do on a write miss?
  When the data block is not in the cache?

## Slide 10: Write Hit Policies
When to propagate new (“dirty”) values to lower levels
  Write-back policy: lazy, take care of it later
  Write-through policy: update lower levels immediately
Write-back policy
  Modify the data in the current cache level only
  When to update the data in the lower level? When cache block is evicted
  Dirty bit per cache block to keep track of blocks that have been updated
Pros
  Write happens at speed of current cache level
  multiple writes to the same block result in only one write back to main memory
Cons
  Evictions take more time
  Data inconsistency between cache and lower levels

## Slide 11: Write Back Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Write Address (32 bits)
V 2
=
&
1
HIT
1
0
0
Dirty
(1 bit)
D 0
D 1
0
Write Data
(8 bits)
1

## Slide 12: Write Back Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Read Address (32 bits)
1
=
&
0
MISS
0
0
0
Dirty
(1 bit)
D 0
D 1
0
DISCARD DATA

## Slide 13: Write Back Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Read Address (32 bits)
1
=
&
0
MISS
0
0
0
Dirty
(1 bit)
D 0
D 1
1
WRITE-BACK DATA

## Slide 14: Write Back Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Write Address (32 bits)
V 2
=
&
1
HIT
1
0
0
Dirty
(1 bit)
D 0
D 1
1
Write Data
(8 bits)
1

## Slide 15: Write Hit Policies
When to propagate new (“dirty”) values to lower levels
  Write-back policy: lazy, take care of it later
  Write-through policy: update lower levels immediately
Write-Through policy
  Update lower levels of cache/memory on every write
  No need for a dirty bit in the cache
Pros
  Reduces complexity of cache (no dirty bit)
  Reads never cause write-backs
  Consistency across levels of memory hierarchy
Cons
  Increased write bandwidth (multiple writes to same block)
  Potentially Increased write latency (wait for write to propagate to lower levels?)

## Slide 16: Write Through Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Write Address (32 bits)
V 2
=
&
1
HIT
1
Write Data
(8 bits)
Write-Through to Lower Level
Update data in cache

## Slide 17: Write Through Cache (32 KB, Direct Mapped, 1 Byte Block)
Block 0
Block 1
Block 2
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag 2
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Read Address (32 bits)
1
=
&
0
MISS
0
DISCARD DATA

## Slide 18: Write Miss Policies
What to do if a write access misses in the cache
  Write allocate policy
  Write no-allocate policy
Write-allocate Policy
  Treat like a read miss, allocate block in cache for data
  Standard write hit actions follow
  Good match for write-back caches
Write no allocate Policy
  Do not allocate a cache block for the write, instead forward write to the next level
  This implies that only a read access will result in allocations
  Goes well with write through policy

## Slide 19: Summary of Write Policies
Write Policy | Hit/Miss | Where is Update Performed
Write Back, Allocate | Hit/Miss | L1
Write Back, No Allocate | Hit | 
Write Back, No Allocate | Miss | 
Write Through, Allocate | Hit/Miss | 
Write Through, No Allocate | Hit | 
Write Through, No Allocate | Miss | 
L1
L2
L1 and L2
L1+L2
L2

## Slide 20: Types of Cache Misses
Compulsory or “cold’’ misses: miss occurs on first access to a memory address
  All the misses that would be incurred by a fully-associative, infinitely sized cache with 1 Byte blocks (assuming Byte addressable memory)
  What is a fully-associate cache: any block can go anywhere! Impractical to implement
Conflict misses: Misses that result as a consequence of limited associativity
  Multiple cache blocks mapping to the same location in the cache
  A fully associative cache has no conflict misses!
Capacity misses: Misses that result as a consequence of finite cache size

## Slide 21: Miss Types

## Slide 22: Cache Performance
Average Memory Access Time (AMAT)
AMATL1 = Hit Access TimeL1 + Miss RateL1 * Miss Access TimeL1
Miss Access TimeL1 = AMATL2
AMATL2 = Hit Access TimeL2 + Miss RateL2 * Miss Access TimeL2
Miss Access TimeL2 = Main Memory Access Time
Compute the AMAT of this memory hierarchy.
AMATL2 = 10 + 0.005*100 = 10.5
AMATL1 = 1 + 0.05*10.5 = 1.525
L1
1 Cycle,
5% miss rate
L2
10 Cycles,
0.5% miss rate
Main Memory (100 cycs)

## Slide 23: Minimizing Miss Rate
Increase cache size, associativity
  Affects cache access time, so AMAT may actually increase!
Increase cache block size
  Trade-off between compulsory and conflict misses
  Pick optimal block size
Multi-level caches (more later)
Other commonly used optimizations
  Victim caches
  Critical word first

## Slide 24: Victim Cache
Direct mapped caches are “cheap” but result in high conflict miss rate
A fully associative cache is expensive, but has low conflict miss rate
A victim cache is a small (4-8 entry) fully associative cache that holds blocks evicted due to conflict misses
  On path between L1 and L2
  Checked on L1 miss
  Hit in victim cache -> swap with block in L1

## Slide 25: 32 KB Direct Mapped Cache with 1 Byte Blocks + Victim Cache
Block 0
Block 1
Mem[A]
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag[A]
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Address B (32 bits)
1
=
MISS
0
&
1
0
Single Entry Victim Cache
Mem[A]
Tag[A]
Mem[B]
Tag[B]
0
1

## Slide 26: 32 KB Direct Mapped Cache with 1 Byte Blocks + Victim Cache
Block 0
Block 1
Mem[A]
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag[A]
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Address A (32 bits)
1
=
MISS
0
&
1
0
Single Entry Victim Cache
Mem[A]
Tag[A]
Mem[B]
Tag[B]
0
1
HIT
Mem[A]
Tag[A]
Mem[B]
Tag[B]

## Slide 27: Multi-Level Caches
L1-I
Instructions only
Unified L2
Both instructions and data
L1-D
Data Only
Partitioned L1-I and L1-D cache
  Reminiscent of Harvard architecture
  Why is this useful?
Inclusive vs. exclusive cache hierarchy
  Inclusive: everything in the L1-I and L1-D caches is also in the L2 cache, but not vice-versa
    Miss in L1 fetches data into both L2 and L1
    Eviction from L1 need not evict from L2
    Eviction from L2 must also evict from L1
    What if L2 block size is larger than L1 block size?
Larger, higher associativity, larger block size

## Slide 28: Software Techniques
Data layout and access patterns can have a significant impact on cache miss rate
  Code can be re-written to exploit the underlying cache hierarchy
  Caution: Might need to be aware of cache parameters
Examples of code optimization to improve cache miss rate:
  Array merging: interleaving the layout of concurrently accessed arrays
  Loop re-ordering
  Blocking

## Slide 29: Array Merging
int a[2048]
int b[2048]
int c[2048]
//Assume every int is 4 Bytes
for (i=0; i<2048; i++)
c[i] = a[i] + b[i];
Block 0
Block 4072
Data Array
(16 bytes)
Block 1
struct merge{
int a;
int b;
int c;
};
struct merge abc[2048]

## Slide 30: Loop Interchange
for (i=0; i<2048; i++)
for (j=0; i<2048; i++)
sum+= a[j][i];
//Arrays stored in column major order
//a[0][0]
//a[0][1]….
//a[1][0] …
Block 0
Block 4072
Data Array
(16 bytes)
Block 1
for (j=0; i<2048; i++)
for (i=0; i<2048; i++)
sum+= a[j][i];

## Slide 31: Blocking
for (i=0; i<N i++)
for (j=0; j<N; j++)
for (k=0; k<; k++)
sum = sum + a[i][k]*b[k][j];
a[0][0]
b[0][1]
a[1][0]
a[0][N-1]
b[0][0]
a[0][1]
b[1][0]
Same elements are being repeatedly reused!
If N is large, by the time the loop gets to a[0][N-1], a[0][0] has been evicted from the cache

## Slide 32: Blocking
a[0][0]
b[0][0]
Partition matrix into B*B sub-blocks such that the sub-blocks fit in the cache
B
B
B
B

## Slide 33
Out-of-order Processing

## Slide 34: WAW Hazard
Assume FP add has 3 cycle latency, FP mult has 6 cycle latency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
IF
ID/RF
EX
EX
EX
EX
EX
EX
MEM
WB
IF
ID/RF
EX
EX
MEM
WB
mul
Rd $f1, $f2
Wrt $f3
nop
add
Rd $f4, $f5
Wrt $f3
Write-after-Write
(WAW) Dependency
What’s the final value in $f3?
EX

## Slide 35: Potential Solution: Stalling
Assume FP add has 3 cycle latency, FP mult has 8 cycle latency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
IF
ID/RF
EX
EX
EX
EX
EX
EX
MEM
WB
IF
ID/RF
EX
EX
MEM
WB
mul
Rd $f1, $f2
Wrt $f3
nop
add
Rd $f4, $f5
Wrt $f3
STALL
EX

## Slide 36: Impact on ILP
Assume FP add has 3 cycle latency, FP mult has 8 cycle latency
Future independent add instructions stall because of the WAW dependency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
add.d $f8, $f6, $f7 // R[$f8] = R[$f6] + R[$f7]
add.d $f11, $f9, $f10 // R[$f11] = R[$f9] + R[$f10]

## Slide 37: Solutions
Use another destination register to eliminate WAW hazard
  But number of architectural registers is limited
Out-of-order (OoO) execution in hardware
  Allows independent instructions whose operands are ready to execute first
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f12 // R[$f3] = R[$f4] + R[$f5]
add.d $f8, $f6, $f7 // R[$f8] = R[$f6] + R[$f7]
add.d $f11, $f9, $f10 // R[$f11] = R[$f9] + R[$f10]

## Slide 38: Enabling OoO Execution
Register renaming in hardware
  Associate a “tag” with the output of each instruction
  Number of tags can be larger than number of architectural regs
Need to buffer instructions till they are ready to execute
  Fetched in order and buffered in “reservation station”
Need to check when an instructions operands are ready
  Each instruction broadcasts its tag when it finishes execution
  Instructions compare their “source tags” (tags of their operands) to see if there is a match
When all source operands of an instruction are ready, dispatch to FU
  Structural hazard if FU is busy

## Slide 39: Tomasulo’s Algorithm
Instruction fetched in order into instruction buffer
And dispatched to reservation station assuming one is free
Instruction wait in reservation stations and monitor common data bus for operand to be available
Arch register file renamed using resv stations

## Slide 40: Register Renaming
Reservation Station
a
b
c
d
Each entry in a reservation station has a tag
When an instruction is assigned to a reservation station, the destination register for that instruction is renamed to the tag of the reservation station
  Architectural registers -> physical registers
  More reservation stations than architectural registers
After renaming, the RS tag is used to refer to that register
Tag

## Slide 41: Register Rename Table
Tag | Value | Valid
 |  | 0/1
One entry for each architectural register
f0
f1
f2
f3
f4
The reservation station entry the register f4 is currently
remapped to
If register is currently not mapped to a reservation station and holds valid data, valid bit is set to 1. Otherwise, the data in the “Value” field is invalid.
Current value of f4 (only if valid bit is set)

## Slide 42: Reservation Station
Tag | Value | Valid
 |  | 0/1
a
b
c
d
Tag from which the value of operand 1 will be obtained
Tag | Value | Valid
 |  | 0/1
Set if value is valid
Value
Operand 1
Operand 2

## Slide 43: Tomasulo’s Algorithm
If a reservation station is available before renaming
  Instruction + renamed operands (tags/value) placed in reservation station
  If reservation station not available, STALL
While in resv stn each instruction
  Monitors CDB for tag of it’s sources
  When tag seen, grab value and keep in the reservation station
  When values for both operands available, ready for dispatch
Dispatch ready instructions to Fus
  Assuming an FU is available, otherwise wait
Once instruction completes execution
  Broadcast value and tag on CDB
  Any Register in the Reg. renaming table with a matching tag updates it value and sets valid bit
Free reservation station