## Slide 1: Computer Architecture I
CS-GY-6133
Topic: Advanced Caches
Instructor: Siddharth Garg

## Slide 2: Types of Cache Misses
Compulsory or “cold’’ misses: miss occurs on first access to a memory address
  All the misses that would be incurred by a fully-associative, infinitely sized cache with 1 Byte blocks (assuming Byte addressable memory)
  What is a fully-associate cache: any block can go anywhere! Impractical to implement
Conflict misses: Misses that result as a consequence of limited associativity
  Multiple cache blocks mapping to the same location in the cache
  A fully associative cache has no conflict misses!
Capacity misses: Misses that result as a consequence of finite cache size

## Slide 3: Miss Types

## Slide 4: Cache Performance
Average Memory Access Time (AMAT)
AMATL1 = Hit Access TimeL1 + Miss RateL1 * Miss Access TimeL1
Miss Access TimeL1 = AMATL2
AMATL2 = Hit Access TimeL2 + Miss RateL2 * Miss Access TimeL2
Miss Access TimeL2 = Main Memory Access Time
Compute the AMAT of this memory hierarchy.
AMATL2 = 10 + 0.005*100 = 10.5
AMATL1 = 1 + 0.05*10.5 = 1.525
L1
1 Cycle,
5% miss rate
L2
10 Cycles,
0.5% miss rate
Main Memory (100 cycs)

## Slide 5: Minimizing Miss Rate
Increase cache size, associativity
  Affects cache access time, so AMAT may actually increase!
Increase cache block size
  Trade-off between compulsory and conflict misses
  Pick optimal block size
Multi-level caches (more later)
Other commonly used optimizations
  Victim caches
  Critical word first

## Slide 6: Victim Cache
Direct mapped caches are “cheap” but result in high conflict miss rate
A fully associative cache is expensive, but has low conflict miss rate
A victim cache is a small (4-8 entry) fully associative cache that holds blocks evicted due to conflict misses
  On path between L1 and L2
  Checked on L1 miss
  Hit in victim cache -> swap with block in L1

## Slide 7: 32 KB Direct Mapped Cache with 1 Byte Blocks + Victim Cache
Block 0
Block 1
Mem[A]
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag[A]
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Address B (32 bits)
1
=
MISS
0
&
1
0
Single Entry Victim Cache
Mem[A]
Tag[A]
Mem[B]
Tag[B]
0
1

## Slide 8: 32 KB Direct Mapped Cache with 1 Byte Blocks + Victim Cache
Block 0
Block 1
Mem[A]
Block 32767
Data Array
(8 bits)
Tag 0
Tag 1
Tag[A]
Tag 32767
Tag Array
(17 bits)
0
0
V..
Valid
(1 bit)
V 0
V 1
Index
(15 bits)
Tag
(17 bits)
Address A (32 bits)
1
=
MISS
0
&
1
0
Single Entry Victim Cache
Mem[A]
Tag[A]
Mem[B]
Tag[B]
0
1
HIT
Mem[A]
Tag[A]
Mem[B]
Tag[B]

## Slide 9: Multi-Level Caches
L1-I
Instructions only
Unified L2
Both instructions and data
L1-D
Data Only
Partitioned L1-I and L1-D cache
  Reminiscent of Harvard architecture
  Why is this useful?
Inclusive vs. exclusive cache hierarchy
  Inclusive: everything in the L1-I and L1-D caches is also in the L2 cache, but not vice-versa
    Miss in L1 fetches data into both L2 and L1
    Eviction from L1 need not evict from L2
    Eviction from L2 must also evict from L1
    What if L2 block size is larger than L1 block size?
Larger, higher associativity, larger block size

## Slide 10: Software Techniques
Data layout and access patterns can have a significant impact on cache miss rate
  Code can be re-written to exploit the underlying cache hierarchy
  Caution: Might need to be aware of cache parameters
Examples of code optimization to improve cache miss rate:
  Array merging: interleaving the layout of concurrently accessed arrays
  Loop re-ordering
  Blocking

## Slide 11: Array Merging
int a[2048]
int b[2048]
int c[2048]
//Assume every int is 4 Bytes
for (i=0; i<2048; i++)
c[i] = a[i] + b[i];
Block 0
Block 4072
Data Array
(16 bytes)
Block 1
struct merge{
int a;
int b;
int c;
};
struct merge abc[2048]

## Slide 12: Loop Interchange
for (i=0; i<2048; i++)
for (j=0; i<2048; i++)
sum+= a[j][i];
//Arrays stored in column major order
//a[0][0]
//a[0][1]….
//a[1][0] …
Block 0
Block 4072
Data Array
(16 bytes)
Block 1
for (j=0; i<2048; i++)
for (i=0; i<2048; i++)
sum+= a[j][i];

## Slide 13: Blocking
for (i=0; i<N i++)
for (j=0; j<N; j++)
for (k=0; k<; k++)
sum = sum + a[i][k]*b[k][j];
a[0][0]
b[0][1]
a[1][0]
a[0][N-1]
b[0][0]
a[0][1]
b[1][0]
Same elements are being repeatedly reused!
If N is large, by the time the loop gets to a[0][N-1], a[0][0] has been evicted from the cache

## Slide 14: Blocking
a[0][0]
b[0][0]
Partition matrix into B*B sub-blocks such that the sub-blocks fit in the cache
B
B
B
B

## Slide 15
Out-of-order Processing

## Slide 16: WAW Hazard
Assume FP add has 3 cycle latency, FP mult has 6 cycle latency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
IF
ID/RF
EX
EX
EX
EX
EX
EX
MEM
WB
IF
ID/RF
EX
EX
MEM
WB
mul
Rd $f1, $f2
Wrt $f3
nop
add
Rd $f4, $f5
Wrt $f3
Write-after-Write
(WAW) Dependency
What’s the final value in $f3?
EX

## Slide 17: Potential Solution: Stalling
Assume FP add has 3 cycle latency, FP mult has 8 cycle latency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
IF
ID/RF
EX
EX
EX
EX
EX
EX
MEM
WB
IF
ID/RF
EX
EX
MEM
WB
mul
Rd $f1, $f2
Wrt $f3
nop
add
Rd $f4, $f5
Wrt $f3
STALL
EX

## Slide 18: Impact on ILP
Assume FP add has 3 cycle latency, FP mult has 8 cycle latency
Future independent add instructions stall because of the WAW dependency
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f3 // R[$f3] = R[$f4] + R[$f5]
add.d $f8, $f6, $f7 // R[$f8] = R[$f6] + R[$f7]
add.d $f11, $f9, $f10 // R[$f11] = R[$f9] + R[$f10]

## Slide 19: Solutions
Use another destination register to eliminate WAW haa
  But number of architectural registers is limited
Out-of-order (OoO) execution in hardware
  Allows independent instructions whose operands are ready to execute first
mul.d $f1, $f2, $f3 // R[$f3] = R[$f1] * R[$f2]
add.d $f4, $f5, $f12 // R[$f3] = R[$f4] + R[$f5]
add.d $f8, $f6, $f7 // R[$f8] = R[$f6] + R[$f7]
add.d $f11, $f9, $f10 // R[$f11] = R[$f9] + R[$f10]

## Slide 20: Enabling OoO Execution
Register renaming in hardware
  Associate a “tag” with the output of each instruction
  Number of tags can be larger than number of architectural regs
Need to buffer instructions till they are ready to execute
  Fetched in order and buffered in “reservation station”
Need to check when an instructions operands are ready
  Each instruction broadcasts its tag when it finishes execution
  Instructions compare their “source tags” (tags of their operands) to see if there is a match
When all source operands of an instruction are ready, dispatch to FU
  Structural hazard if FU is busy

## Slide 21: Tomasulo’s Algorithm
Instruction fetched in order into instruction buffer
And dispatched to reservation station assuming one is free
Instruction wait in reservation stations and monitor common data bus for operand to be available
Arch register file renamed using resv stations

## Slide 22: Register Renaming
Reservation Station
a
b
c
d
Each entry in a reservation station has a tag
When an instruction is assigned to a reservation station, the destination register for that instruction is renamed to the tag of the reservation station
  Architectural registers -> physical registers
  More reservation stations than architectural registers
After renaming, the RS tag is used to refer to that register
Tag

## Slide 23: Register Rename Table
Tag | Value | Valid
 |  | 0/1
One entry for each architectural register
f0
f1
f2
f3
f4
The reservation station entry the register f4 is currently
remapped to
Alternatively, if register is currently not mapped to a reservation station and holds valid data, valid bit is set to 1
Current value of f4 (only if valid bit is set)

## Slide 24: Reservation Station
Tag | Value | Valid
 |  | 0/1
a
b
c
d
Tag from which the value of operand 1 will be obtained
Tag | Value | Valid
 |  | 0/1
Set if value is valid
Value

## Slide 25: Tomasulo’s Algorithm
If a reservation station is available before renaming
  Instruction + renamed operands (tags/value) placed in reservation station
  If reservation station not available, STALL
While in resv stn each instruction
  Monitors CDB for tag of it’s sources
  When tag seen, grab value and keep in the reservation station
  When values for both operands available, ready for dispatch
Dispatch ready instructions to Fus
  Assuming an FU is available, otherwise wait
Once instruction completes execution
  Broadcast value and tag on CDB
  Any Register in the Reg. renaming table with a matching tag updates it value and sets valid bit
Free reservation station

## Slide 26: Example
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
F
D
EX
W
F: Fetch instruction
D: Decode, Rename
E: Execute (when operands ready), multi-cycle
W: Broadcast result on CDB

## Slide 27: Example
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
F
D
EX
WB
F: Fetch instruction
D: Decode, Rename
E: Execute (when operands ready), multi-cycle
WB: Broadcast result on CDB

## Slide 28: Cycle 0
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
 |  | 0
 |  | 0
x
y
Tag | Value | Valid
 |  | 0
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | .. | ..
 | .. | ..
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5

## Slide 29: Cycle 1
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
 |  | 0
 |  | 0
x
y
Tag | Value | Valid
 |  | 0
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
 | 3 | 1
 | .. | ..
 | .. | ..
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
F

## Slide 30: Cycle 2
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
 |  | 0
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
~ | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
~ | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
 | .. | ..
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
D
F
Resv Stn x ready to execute

## Slide 31: Cycle 3
Tag | Value | Valid
x | ~ | 0
 |  | 0
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
~ | 4 | 1
 |  | 0
 |  | 0
 |  | 0
Tag | Value | Valid
~ | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
~ | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
D
F
E1

## Slide 32: Cycle 4
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
 |  | 0
 |  | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
 |  | 0
 |  | 0
Tag | Value | Valid
-- | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
-- | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
 | .. | 1
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11,
W
D
E2
F
Resv Stn b ready to execute

## Slide 33: Cycle 5
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
 |  | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
 |  | 0
Tag | Value | Valid
-- | 1 | 1
 |  | 0
x
y
Tag | Value | Valid
-- | 2 | 1
 |  | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
 | 11 | 1
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
E1
E3
F
D
Resv Stn c ready to execute

## Slide 34: Cycle 6
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
 |  | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
 |  | 0
Tag | Value | Valid
-- | 1 | 1
b | ~ | 0
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
a | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
E2
E4
F
E1
D

## Slide 35: Cycle 7
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
b | ~ | 0
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
E3
E5
D
E2
W
Note that f5 is remapped from a to d

## Slide 36: Cycle 9
Tag | Value | Valid
x | -- | 0
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
b | ~ | 0
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8

## Slide 37: Cycle 9
Tag | Value | Valid
~ | 2 | 1
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
~ | 8 | 1
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
Update all resv stn entries
waiting for tags x and b

## Slide 38: Cycle 9
Tag | Value | Valid
~ | 2 | 1
~ | 2 | 1
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | 6 | 1
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | 1 | 1
~ | 8 | 1
x
y
Tag | Value | Valid
-- | 2 | 1
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
~ | 2 | 1
 | .. | ..
d | .. | 0
~ | 8 | 1
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
Update RF entries currently mapped
to tags x and b

## Slide 39: Cycle 9
Tag | Value | Valid
~ | 2 | 1
~ | ~ | 0
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | ~ | 0
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | ~ | 0
~ | 8 | 1
x
y
Tag | Value | Valid
~ | ~ | 0
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
W
WB
WB
W
E4
W
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
Release resv. stns x and b
Resv station a is ready to be scheduled!

## Slide 40: Future Cycle
Tag | Value | Valid
~ | 2 | 1
~ | ~ | 0
~ | 8 | 1
a | ~ | 0
a
b
c
d
Tag | Value | Valid
-- | 4 | 1
~ | ~ | 0
~ | 9 | 1
y | ~ | 0
Tag | Value | Valid
-- | ~ | 0
~ | 8 | 1
x
y
Tag | Value | Valid
~ | ~ | 0
c | ~ | 0
FP MULT (6 cycles)
FP ADD (4 cycles)
Tag | Value | Valid
 | 1 | 1
 | 2 | 1
x | 3 | 0
 | .. | ..
d | .. | 0
b |  | 0
 | .. | 
 | .. | 
c | .. | 0
y | 11 | 0
f1
f2
f11
muld f1, f2, f3
addd f3, f4, f5
addd f2, f6, f7
addd f8, f9, f10
muld f7, f10, f11
addd f5, f11, f5
WB
WB Tag x, Data = 2*1 = 2
WB Tag b, Data = 2+6 = 8
When resv a completes execution, its value is sent to operand in resv stn d but not updated in RF. Why?